## Slide 1
PI and Thermal Simulation Study for BD95861MUV Board
January 07th, 2014
Hosted by: Xuan Dang

## Slide 2
Agenda
  Introduction
  DC Drop Analysis
  Current Density Analysis
  Thermal Analysis
  Conclusion

## Slide 3
Introduction
This work considers power simulation and thermal simulation on BD95861MUV boards.
  Based on board file BD95861MUVEVK-101_EVAL_BRD_REV02_20140107_1800.brd
Hyperlynx v8.2.1 and Hyperlynx Thermal v9.1 (MentorGraphic) software is used for simulation
PI simulation considers:
  DC Drop analysis
    Determine what the max drop for power rail
  Current Density analysis
    Determine the hot spot of current density on PCB
Thermal simulation considers:
    PCB temperature profile including consideration for conductive, radiative, and convective heat transfer

## Slide 4
BD95861MUV Board
Based on the board file : BD95861MUVEVK-101_EVAL_BRD_REV02_20140107_1800.brd
Vin 5V/div (DC)

## Slide 5
BD95861MUV Schematic
Based on the schematic file : BD95861MUV_EVAL_SCH_REV02_20140107_1800.pdf

## Slide 6
BD95861MUV Board power consumption
Device/rail | Source/VRM refdes | Source PCB netname | Sink/load PCB refdes | Load PCB net name | Nominal Voltage(V) | Voltage tolerance (%) | Max current (A) | Power input (W) | Power consumption (W) | Note
Power input via TP1/TP3 connectors (VIN 7.5-18V) | TP1 | VIN | U1 | VIN | 7.50 |  | 5.00 | 37.50 |  | Max input current = (Pout + PONH + PONL + PL)/VIN = 4.44A with Vin =7.5V (worst condition). So we choose max input current =5A to simulate power/thermal
Power dissipation on BD95861MUV internal FETs | TP1 | VIN | U1 | VIN |  |  | 6.00 |  | 3.12 | RONH=0.1 Ohm; RONL=0.06 Ohm
Power dissipation on inductor L1 | ZX1 | SW | L1 | SW_ZX |  |  | 6.00 |  | 0.68 | RL = 0.019 Ohm
Power consumption at load via connector TP2/TP4 (VOUT 5V) | L1 | VOUT | TP2 | VOUT | 5 | 2 | 6.00 |  | 30.00 | 
 |  |  |  |  |  |  | Total | 37.50 | 33.80 | 

## Slide 7
Current Density analysis for VIN7.5V@5A
Max Current Density 31.9mA/mil2 < 40mA/mil2 (This rule limit 10 0C of temperature rise above ambient)  Copper planes for VIN is OK
Source TP1
Load U1

## Slide 8
DC Drop analysis for VIN7.5V@5A
Max DC Drop 6.0mV < 150mV (2% tolerance of 7.5V)  Copper planes for VIN is OK
Source TP1
Load U1

## Slide 9
Current Density analysis for SW@6A
Max Current Density 40.9mA/mil2 ~ 40mA/mil2 (This rule limit 10 0C of temperature rise above ambient)  Copper plane for SW is OK
Source U1
Load L1
Solder-shorted ZX1

## Slide 10
DC Drop analysis for SW@6A
Max DC Drop 0.7 mV < 120mV (2% tolerance of assumption voltage 6V)  Copper planes for SW is OK
Source U1
Load L1
Solder-shorted ZX1

## Slide 11
Current Density analysis for VOUT 5V@6A
Max Current Density 61.3mA/mil2 > 40mA/mil2 (This rule limit 10 0C of temperature rise above ambient)  We reduced VOUT’s current density as possible
Source L1
Load TP2

## Slide 12
DC Drop analysis for VOUT 5V@6A
Max DC Drop 2.0 mV < 100mV (2% tolerance of 5V)  Copper planes for VOUT is OK
Source L1
Load TP2

## Slide 13
Thermal Analysis
SW 5V/div
Environment conditions
  Air Temperature : 25 0C , 35 0C and 45 0C
  Air Pressure: 1 atm
  Gravity: 1
  Humidity ratio: 0.5%
  No incoming air flow (Natural convection)
  Emissivity of board: 1
  Board location : single board
  System: closed

## Slide 14
Thermal Analysis (Con’t)
VOUT 20mV/div (AC)
SW 5V/div
Component properties
 | BD96861MUV | SPM6530T-2R2M | RB085B-30TL (Diode D3) | SML-310MTT86 | SST2222AT116
Number of pins | 25 | 2 | 3 | 2 | 3
Pin length | 0.028” | 0.134” | 0.063 | 0.032 | 0.05
Pin width | 0.012” | 0.073” | 0.019 | 0.032 | 0.04
Pin thickness | 0.009” | 0.006 | 0.02 | 0.01 | 0.005
Pin thermal conductivity | 223.031Btu/hrftF | 223.031Btu/hrftF | 223.031Btu/hrftF | 223.031Btu/hrftF | 223.031Btu/hrftF
Max. power dissipation | 3.12 W (at Vin=7.5V) 2.76W (at Vin=12V) | 0.684 W | 2.88 W | 0.044 W | 0.012 W

## Slide 15
Thermal Analysis (Con’t)
  Air temperature 250C, power dissipation of BD95861MUV is 3.12W (at VIN=7.5V), exclude power dissipation of DNP diode D3 RB085B-30TL
L1: SPM6530T-2R2M
Max. power dissipation: 0.684 W
Component temperature = 56.7 0C
U1: BD95861MUV
Max. power dissipation: 3.12 W @VIN=7.5V
Component temperature = 70 0C
U1
The highest temperature on board is about 60.1 0C
The highest temperature on component is on BD95861MUV ( about 70 0C)
L1
D3
D3:RB085B-30TL
Component temperature = 55.5 0C

## Slide 16
Thermal Analysis (Con’t)
  Air temperature 350C, power dissipation of BD95861MUV is 3.12W (at VIN=7.5V), exclude power dissipation of DNP diode D3 RB085B-30TL
L1: SPM6530T-2R2M
Max. power dissipation: 0.684 W
Component temperature = 62.8 0C
U1: BD95861MUV
Max. power dissipation: 3.12 W @VIN=7.5V
Component temperature = 76.2 0C
The highest temperature on board is about 66.2 0C
The highest temperature on component is on BD95861MUV ( about 76.2 0C)
D3:RB085B-30TL
Component temperature = 61.7 0C
U1
L1
D3

## Slide 17
Thermal Analysis (Con’t)
  Air temperature 450C, power dissipation of BD95861MUV is 3.12W (at VIN=7.5V), exclude power dissipation of DNP diode D3 RB085B-30TL
L1: SPM6530T-2R2M
Max. power dissipation: 0.684 W
Component temperature = 69 0C
U1: BD95861MUV
Max. power dissipation: 3.12 W @VIN=7.5V
Component temperature = 82.4 0C
The highest temperature on board is about 72.4 0C
The highest temperature on component is on BD95861MUV ( about 82.4 0C)
D3:RB085B-30TL
Component temperature = 67.9 0C
U1
L1
D3

## Slide 18
Thermal Analysis (Con’t)
  Air temperature 250C, power dissipation of BD95861MUV is 3.12W (at VIN=7.5V), include power dissipation of DNP diode D3 RB085B-30TL
L1: SPM6530T-2R2M
Max. power dissipation: 0.684 W
Component temperature = 86.2 0C
U1: BD95861MUV
Max. power dissipation: 3.12 W @VIN=7.5V
Component temperature = 98.9 0C
The highest temperature on board is about 89.2 0C
The highest temperature on component is on BD95861MUV ( about 98.9 0C)
D3:RB085B-30TL
Max. power dissipation: 2.88 W
Component temperature = 90.3 0C
U1
L1
D3

## Slide 19
Thermal Analysis (Con’t)
  Air temperature 350C, power dissipation of BD95861MUV is 3.12W (at VIN=7.5V), include power dissipation of DNP diode D3 RB085B-30TL
L1: SPM6530T-2R2M
Max. power dissipation: 0.684 W
Component temperature = 91.9 0C
U1: BD95861MUV
Max. power dissipation: 3.12 W @VIN=7.5V
Component temperature = 104.7 0C
The highest temperature on board is about 94.9 0C
The highest temperature on component is on BD95861MUV ( about 104.7 0C)
D3:RB085B-30TL
Max. power dissipation: 2.88 W
Component temperature = 96 0C
U1
L1
D3

## Slide 20
Thermal Analysis (Con’t)
  Air temperature 450C, power dissipation of BD95861MUV is 3.12W (at VIN=7.5V), include power dissipation of DNP diode D3 RB085B-30TL
L1: SPM6530T-2R2M
Max. power dissipation: 0.684 W
Component temperature = 97.6 0C
U1: BD95861MUV
Max. power dissipation: 3.12 W @VIN=7.5V
Component temperature = 110.3 0C
The highest temperature on board is about 100 0C
The highest temperature on component is on BD95861MUV ( about 110.3 0C)
D3:RB085B-30TL
Max. power dissipation: 2.88 W
Component temperature = 101.7 0C
U1
L1
D3

## Slide 21
Thermal Analysis (Con’t)
  Air temperature 250C, power dissipation of BD95861MUV is 2.76 W (at VIN=12V), exclude power dissipation of DNP diode D3 RB085B-30TL
L1: SPM6530T-2R2M
Max. power dissipation: 0.684 W
Component temperature = 53.3 0C
U1: BD95861MUV
Max. power dissipation: 2.76 W @VIN=12V
Component temperature = 64.8 0C
The highest temperature on board is about 56 0C
The highest temperature on component is on BD95861MUV ( about 64.8 0C)
D3:RB085B-30TL
Component temperature = 52 0C
U1
L1
D3

## Slide 22
Thermal Analysis (Con’t)
  Air temperature 350C, power dissipation of BD95861MUV is 2.76 W (at VIN=12V), exclude power dissipation of DNP diode D3 RB085B-30TL
L1: SPM6530T-2R2M
Max. power dissipation: 0.684 W
Component temperature = 59.5 0C
U1: BD95861MUV
Max. power dissipation: 2.76 W @VIN=12V
Component temperature = 71 0C
The highest temperature on board is about 62.2 0C
The highest temperature on component is on BD95861MUV ( about 71 0C)
D3:RB085B-30TL
Component temperature = 58.2 0C
U1
L1
D3

## Slide 23
Thermal Analysis (Con’t)
  Air temperature 450C, power dissipation of BD95861MUV is 2.76 W (at VIN=12V), exclude power dissipation of DNP diode D3 RB085B-30TL
L1: SPM6530T-2R2M
Max. power dissipation: 0.684 W
Component temperature = 65.8 0C
U1: BD95861MUV
Max. power dissipation: 2.76 W @VIN=12V
Component temperature = 77.3 0C
The highest temperature on board is about 68.5 0C
The highest temperature on component is on BD95861MUV ( about 77.3 0C)
D3:RB085B-30TL
Component temperature = 64.5 0C
U1
L1
D3

## Slide 24
Thermal Analysis (Con’t)
  Air temperature 250C, power dissipation of BD95861MUV is 2.76 W (at VIN=12V), include power dissipation of DNP diode D3 RB085B-30TL
L1: SPM6530T-2R2M
Max. power dissipation: 0.684 W
Component temperature = 83.2 0C
U1: BD95861MUV
Max. power dissipation: 2.76 W @VIN=12V
Component temperature = 94.1 0C
The highest temperature on board is about 85.8 0C
The highest temperature on component is on BD95861MUV ( about 94.1 0C)
D3:RB085B-30TL
Max. power dissipation: 2.88 W
Component temperature = 87.2 0C
U1
L1
D3

## Slide 25
Thermal Analysis (Con’t)
  Air temperature 350C, power dissipation of BD95861MUV is 2.76 W (at VIN=12V), include power dissipation of DNP diode D3 RB085B-30TL
L1: SPM6530T-2R2M
Max. power dissipation: 0.684 W
Component temperature = 88.9 0C
U1: BD95861MUV
Max. power dissipation: 2.76 W @VIN=12V
Component temperature = 99.8 0C
The highest temperature on board is about 91.5 0C
The highest temperature on component is on BD95861MUV ( about 99.8 0C)
D3:RB085B-30TL
Max. power dissipation: 2.88 W
Component temperature = 92.9 0C
U1
L1
D3

## Slide 26
Thermal Analysis (Con’t)
  Air temperature 450C, power dissipation of BD95861MUV is 2.76 W (at VIN=12V), include power dissipation of DNP diode D3 RB085B-30TL
L1: SPM6530T-2R2M
Max. power dissipation: 0.684 W
Component temperature = 94.7 0C
U1: BD95861MUV
Max. power dissipation: 2.76 W @VIN=12V
Component temperature = 105.6 0C
The highest temperature on board is about 97.3 0C
The highest temperature on component is on BD95861MUV ( about 105.6 0C)
D3:RB085B-30TL
Max. power dissipation: 2.88 W
Component temperature = 98.7 0C
U1
L1
D3

## Slide 27
Summary
The PI simulation shows that the max. amount voltage drop of VIN power is 6.0mV, the max. current density of VIN power is 31.9mA/mil2; the max. amount voltage drop of SW power is 0.7mV, the max. current density of SW power is 40.9mA/mil2; the max. amount voltage drop of VOUT power is 2.0mV, the max. current density of VOUT power is 61.3mA/mil2
The highest temperature of BD95861MUV can be reached temperature as table below:
 | VIN=7.5V |  | VIN=12V | 
 | D2, D3: not install | D2, D3: install | D2, D3: not install | D2, D3: install
Air temperature: 250C | 70 0C | 98.9 0C | 64.8 0C | 94.1 0C
Air temperature: 350C | 76.2 0C | 104.7 0C | 71 0C | 99.8 0C
Air temperature: 450C | 82.4 0C | 110.3 0C | 77.3 0C | 105.6 0C